## Slide 1
SLIIT FACULTY OF COMPUTING | CDAP RESEARCH PROJECT R26-IT-162
FloodSense AI: Intelligent IoT Microclimate Sensing & Dual-Stage Predictive Flood Inundation Modeling
Hyperlocal Rainfall Forecasting & Distance-Based Dynamic Risk Scoring for Kelani River Basin Communities
STUDENT A: EMBEDDED IOT & RAINFALL ML ENGINE
Rasara S.H.K. (IT21313998)
• Hardware: ESP32 Microcontroller + Calibrated Tipping Bucket Rain Gauge • Cloud Messaging: Lightweight MQTT Telemetry over HiveMQ Cloud Broker • Atmospheric Fusion: 14 Open-Meteo Synoptic Weather Variables • ML Models: LightGBM & XGBoost Multi-Horizon Forecasting (24h, 48h, 72h)
STUDENT B: TWO-STAGE FLOOD RISK & SAAS UI
U.H.K. Sankalana (IT22236814)
• Risk Algorithm: Distance-Based Dynamic Flood Risk Personalization (DFRS) • ML Pipeline: Two-Stage XGBoost (Stage 1A Classifier, 1B Risk Regressor) • Hydrology Output: Stage 2 Multi-Output (Inundation Arrival Time & Water Depth) • Web Interface: Modern React Dashboard with Trilingual Notification Alerts
SLIIT CDAP R26-IT-162 | FloodSense AI (Kelani River Basin Early Warning) | Slide 1 of 13

## Slide 2
PROBLEM CONTEXT & SOCIO-ECONOMIC IMPACT
The Kelani River Basin Flood Crisis & The Early Warning Deficit
500,000+ vulnerable citizens face recurring catastrophic monsoonal inundation with inadequate warning lead time
500,000+
Vulnerable Citizens
Across Colombo, Gampaha & Kegalle
LKR 50B+
Annual Economic Loss
Infrastructure, property & crop damage
300,000+
Displaced Annually
Major events in 2016, 2021 & 2024
6–12 Hours
Current Warning Gap
Synoptic forecasts lack micro-catchment resolution
LIMITATIONS OF CURRENT DISASTER SYSTEMS
• Coarse Spatial Resolution: 25 km synoptic weather grids miss localized convective micro-catchment cloudbursts. • Manual Gauge Reporting: Gauge readings are collected manually every 6–12 hours, creating fatal latency. • Binary Blanket Alerts: DMC alerts simply state 'Kelani Basin Flood Alert' without telling a family if water will reach their specific doorstep or in how many hours. • No Water Depth or Arrival Estimation: No actionable metrics for evacuation planning or asset protection.
OUR INTEGRATED AI & IOT PARADIGM
• Sub-Kilometer Microclimate Sensing: Real-time calibrated tipping buckets streaming live rain intensity via MQTT. • Atmospheric Fusion AI: Fuses 14 synoptic weather variables to project 24h, 48h, and 72h antecedent rainfall depths. • Two-Stage Inundation Intelligence: Evaluates localized occurrence (Yes/No), continuous risk score (0–100), arrival time (hours), and inundation depth (meters). • Trilingual Decision Support: Automated alerts dispatched in Sinhala, Tamil, and English with community evacuation SOPs.
SLIIT CDAP R26-IT-162 | FloodSense AI (Kelani River Basin Early Warning) | Slide 2 of 13

## Slide 3
REVIEWER FEEDBACK & SYSTEM EVOLUTION
How We Addressed Panel Comments & Upgraded the Research
Systematic progression from a basic monitoring prototype to an enterprise-grade AI flood early warning system
01. DETECTION & SENSING
From: Single sensor & basic monitoring ➔ To: Multi-factor IoT sensing array (calibrated tipping bucket, reed switch debouncing ISR, Open-Meteo 14-variable live atmospheric fusion).
02. DATA PIPELINE
From: Manual logs & once-a-day polling ➔ To: Sub-second MQTT streaming via HiveMQ Cloud Broker with local non-volatile buffering and automatic reconnect watchdog.
03. PREDICTIVE CAPABILITY
From: Binary flood alerts (Yes / No) ➔ To: Dual-stage ML pipeline providing continuous risk score (0–100%), arrival time in hours, and water height with cm precision.
04. TARGETED BENEFICIARIES
From: Generic text notifications ➔ To: Personalized Distance-Based Dynamic Risk Scoring (DFRS) with automated trilingual notifications (Sinhala, Tamil, English).
SLIIT CDAP R26-IT-162 | FloodSense AI (Kelani River Basin Early Warning) | Slide 3 of 13

## Slide 4
SYSTEM ARCHITECTURE & DATA FLOW
The Integrated Symbiotic Pipeline: Sensor to Inundation Decision
Seamless cross-tier data pipeline connecting Student A's IoT & ML engine with Student B's flood risk models
LAYER 1: SENSING & TELEMETRY
Component A (Rasara)
• ESP32 Microcontroller (GPIO 4)
• Tipping Bucket (0.2 mm/tip)
• 100 ms Hardware/Software Debounce
• HiveMQ MQTT Cloud Broker
• JSON Payload Serialization
LAYER 2: FUSION & RAINFALL ML
Component A (Rasara)
• Open-Meteo Live Synoptic API
• 14 Atmospheric Variables (CAPE, RH)
• 168h Antecedent Rolling Buffers
• LightGBM Multi-Horizon Predictor
• Forecasts: 24h, 48h, 72h Depths
LAYER 3: TWO-STAGE FLOOD ML
Component B (Sankalana)
• Stage 1A: XGBoost Classifier
• Evaluates Flood Occurrence (Yes/No)
• Stage 1B: XGBoost Regressor (0-100)
• Stage 2: Multi-Output Regressor
• Predicts: Arrival Time & Water Depth
LAYER 4: DECISION SUPPORT
Component B (Sankalana)
• Distance-Based Proximity Engine
• Modern React Dashboard UI
• Live SVG Risk Dials & Audits
• Automated Trilingual Alert Dispatch
• DMC Civil Defense SOP Guidance
SLIIT CDAP R26-IT-162 | FloodSense AI (Kelani River Basin Early Warning) | Slide 4 of 13

## Slide 5
COMPONENT A | RASARA S.H.K. (IT21313998)
Embedded IoT Microclimate Sensing & Edge Telemetry Firmware
High-frequency rainfall pulse detection with hardware debouncing and resilient cloud messaging
HARDWARE ARCHITECTURE
• MCU: ESP32 dual-core Xtensa 32-bit LX6 running at 240 MHz with 520 KB SRAM.
• Rain Sensor: Dual-chamber tipping bucket rain collector with magnetic reed switch.
• Physical Calibration: 0.20 mm displacement per mechanical tip (funnel area 32,429 mm²).
• Microclimate Module: DHT22 / BME280 temperature and relative humidity monitoring.
• Power Subsystem: 3.7V 18650 Li-ion battery with 6V 5W solar panel and TP4056 charge IC.
SIGNAL PROCESSING & ISR
• Interrupt Service Routine (ISR): Bound to GPIO 4 (FALLING edge), executed in high-speed IRAM.
• Software Debouncing: Enforces a 100 ms threshold to eliminate reed switch contact chatter oscillations.
• Intensity Calculation: Computes rainfall intensity dynamically based on pulse arrival frequency.
• Median Filter: 5-sample moving median filter prevents false positive spikes from debris.
• Watchdog Timer: Automatic hardware recovery resets the microcontroller if network hangs.
MQTT CLOUD TELEMETRY
• Protocol: MQTT v3.1.1 (lightweight 2-byte header overhead vs 800-byte HTTP REST).
• Cloud Broker: HiveMQ Cloud cluster (broker.hivemq.com:1883, topic: 'Smart Irrigation Hive/data').
• Telemetry Payload: Serialized JSON with device ID, tip count, rainfall rate, temperature & battery.
• Local Storage Fallback: Non-volatile SPIFFS flash logs data if cellular connection drops.
• Ingestion Latency: Sub-second (typically <280 ms) cloud ingestion from edge to backend.
SLIIT CDAP R26-IT-162 | FloodSense AI (Kelani River Basin Early Warning) | Slide 5 of 13

## Slide 6
COMPONENT A | RASARA S.H.K. (IT21313998)
Multi-Horizon Machine Learning Rainfall Forecasting Engine
Coupling atmospheric reanalysis with edge telemetry to predict 24h, 48h, and 72h precipitation depths
DATA FUSION & FEATURE ENGINEERING PIPELINE
• 14 Atmospheric Variables: Real-time ECMWF/GFS grids from Open-Meteo (CAPE, 2m temp, surface pressure, relative humidity, cloud cover, dew point).
• Wind Vector Decomposition: 10m wind speed and direction transformed into orthogonal vectors u = -s·sin(θ) and v = -s·cos(θ) to capture monsoonal moisture advection.
• Antecedent Rolling Windows: 1h, 3h, 6h, 12h, 24h, 48h, 72h, and 7-day cumulative rainfall and moving variances.
• Antecedent Precipitation Index (API): Models soil moisture depletion across continuous days (recession constant k = 0.88).
• Cyclical Manifold Encodings: Sine and cosine harmonics encode day-of-year and hour-of-day, preserving monsoonal continuity.
• Data Leakage Prevention: Evaluated strictly with TimeSeriesSplit (n_splits=5); zero lookahead bias.
MODEL BENCHMARKS & EVALUATION RESULTS
Comparative Multi-Horizon Benchmark (Day 1 / 24h Horizon):
🏆 LightGBM Regressor: R² = 0.841 | MAE = 2.84 mm | RMSE = 4.12 mm
🥈 XGBoost Regressor: R² = 0.835 | MAE = 2.98 mm | RMSE = 4.25 mm
🥉 Random Forest: R² = 0.792 | MAE = 3.65 mm | RMSE = 5.10 mm
• Ridge Linear Baseline: R² = 0.648 | MAE = 5.82 mm | RMSE = 7.40 mm
Key Research Findings:
• LightGBM's Gradient-based One-Side Sampling (GOSS) and Exclusive Feature Bundling (EFB) achieved 30ms inference latency on commodity CPUs.
• Rain Occurrence Classification: F1-score of 0.912 and ROC-AUC of 0.945.
• Automated Payload Handoff: Model aggregates 7-day total and peak intensity, feeding directly into Student B's flood model.
SLIIT CDAP R26-IT-162 | FloodSense AI (Kelani River Basin Early Warning) | Slide 6 of 13

## Slide 7
COMPONENT B | U.H.K. SANKALANA (IT22236814)
Two-Stage Machine Learning Dynamic Flood Risk & Inundation Model
Combining hydro-topographic vectors with rainfall predictions to compute occurrence, risk score, arrival time, and depth
STAGE 1A: BINARY CLASSIFIER
• Model: XGBoost Classifier (stage1_classifier.json)
• Task: Evaluates whether a flood will physically occur (Yes / No).
• Bayesian Posterior: Computes calibrated probability P(Flood).
• F1-Score: 0.941 across 10-year historical Kelani validation callset.
• Top Split Features: 7-day rainfall total and peak storm intensity (from Student A).
STAGE 1B: RISK REGRESSOR
• Model: XGBoost Regressor (stage1_risk_regressor.json)
• Task: Produces continuous 0 to 100 Flood Risk Score.
• RMSE: 3.12 (on 0–100 scale).
• Severity Tiers:
- Very High: Score ≥ 70 (Evacuation)
- High: Score 50 – 69 (Severe Alert)
- Moderate: Score 30 – 49 (Monitor)
- Low: Score < 30 (Baseline Safe)
STAGE 2: MULTI-OUTPUT
• Model: MultiOutput XGBoost Regressor (Executes only if Stage 1A = Yes)
• Metric 1: Inundation Arrival Time (hours until wavefront hits community locus).
• Metric 2: Peak Inundation Height (water depth in meters above ground level).
• Physical Damping: Integrates terrain elevation, river distance, and soil permeability.
SLIIT CDAP R26-IT-162 | FloodSense AI (Kelani River Basin Early Warning) | Slide 7 of 13

## Slide 8
COMPONENT B | U.H.K. SANKALANA (IT22236814)
Distance-Based Dynamic Flood Risk Personalization (DFRS)
Hyperlocal spatial proximity modeling, executive React dashboard UI, and trilingual community alerts
DISTANCE-BASED DYNAMIC FLOOD RISK (DFRS)
• Proximity Decay Formulation: Risk score dynamically scales as Euclidean distance to the active river channel decreases.
• Geospatial Feature Integration: Couples elevation (DEM/SRTM), soil classification (Clay vs Sandy), and land cover (Urban vs Agricultural).
• Sedawatta / Grandpass Reach (High Risk): River distance = 45m, elevation = 3.2m ➔ Triggers rapid arrival alert (3.4 hours, 3.84m depth).
• Malabe Elevated Reach (Safe): River distance = 1,250m, elevation = 32m ➔ Low risk score (<25%), normal baseline status.
EXECUTIVE REACT DASHBOARD & MULTILINGUAL ALERTS
• Responsive Vite React Architecture: Built with Tailwind CSS, Plus Jakarta Sans typography, and SVG semi-circular risk dials.
• Live Backend Health Monitor: Real-time pulsing badge checks Flask ML inference engine (/api/health) on port 5000.
• 1-Click Viva Presets: Instant scenario buttons for Colombo Lower Reach (Sedawatta), Ja-Ela Plain, and Malabe Inland.
• Trilingual Automated Alerts: Dispatches localized emergency directives in Sinhala, Tamil, and English via SMS & push notifications.
• DMC SOP Guidelines: Displays actionable mitigation steps (boat mobilization, electrical de-energizing) based on predicted depth.
SLIIT CDAP R26-IT-162 | FloodSense AI (Kelani River Basin Early Warning) | Slide 8 of 13

## Slide 9
CROSS-SYSTEM INTEGRATION & DATA CONTRACT
How Component A Feeds Component B in Real-Time
The automated mapping pipeline transforming multi-horizon rainfall forecasts into the 12-feature flood matrix
THE 12-FEATURE DATA HAND-OFF CONTRACT
Component A (Student A) passes 3 primary dynamic hydrometeorological features via REST API & In-Process Bridge:
1. rainfall_7d_mm = round(rain_cum72h * 1.8 + rain_24h, 2) ➔ Cumulative antecedent saturation (200 mm)
2. monthly_rainfall_mm = round(rain_cum72h * 4.2 + 80.0, 2) ➔ 30-day baseline ground saturation (350 mm)
3. rainfall_intensity_mmhr = round(iot_rate * 3.5, 2) ➔ Peak storm cloudburst intensity (15–28 mm/hr)
Component B (Student B) combines these with 9 geospatial & catchment features:
• district: Colombo / Gampaha • latitude & longitude: GPS WGS84 coordinates
• elevation_m: Topographic elevation • distance_to_river_m: Proximity to active channel
• landcover: Urban, Agriculture • soil_type: Clay, Loamy, Sandy
• historical_flood_count: DMC records • river_flow_rate_m3s: Upstream hydrometric discharge
Execution Result:
➔ Clicking '⚡ Sync IoT Rainfall' in React UI instantly binds Component A's forecast into Component B's Two-Stage XGBoost model, producing Occurrence = YES, Risk = 56.92%, Arrival = 3.41h, Height = 3.84m.
SLIIT CDAP R26-IT-162 | FloodSense AI (Kelani River Basin Early Warning) | Slide 9 of 13

## Slide 10
EMPIRICAL VALIDATION & COMMUNITY FIELD TRIALS
Field Testing Across Kelani Riverine Communities & Post-Test Iterations
Tested over 3 weeks across 3 agricultural riverine locations capturing 12 real monsoon rainfall events
FIELD TRIAL PROTOCOL
• Locations: Sedawatta (Lower Reach), Hanwella (Mid Reach), Kaduwela (Lowland Plain).
• Participants: 15 riverine households, 5 local farmers, 2 local disaster response coordinators.
• Duration: 3-week continuous monitoring period during South-West monsoon burst.
• Events Captured: 12 independent rainfall pulses ranging from 12 mm to 145 mm/day.
USER EVALUATION SCORES
• Overall Satisfaction: 4.4 / 5.0
• Timeliness of Alert: 4.6 / 5.0 (Average 4.2 hours actionable lead time).
• Language Clarity: 4.8 / 5.0 (Trilingual Sinhala & Tamil alerts highly praised).
• Usability of Web UI: 4.3 / 5.0 (Clear color-coded risk dials appreciated by officers).
• False Alarm Rate: Low (<8.3%), far superior to regional blanket warnings.
POST-TESTING ITERATIONS
• Request: Prevent false tip triggers from wind-blown tree debris. ➔ Action: Added 5-sample median filtering in firmware.
• Request: Adjustable risk sensitivity for elevated farmers. ➔ Action: Added configurable distance weighting in DFRS.
• Request: Longer off-grid battery resilience in severe overcast. ➔ Action: Optimized deep sleep cycling, extending battery life to 90 days.
SLIIT CDAP R26-IT-162 | FloodSense AI (Kelani River Basin Early Warning) | Slide 10 of 13

## Slide 11
COMMERCIALIZATION & MARKET FEASIBILITY
Business Model, Unit Economics & 3-Year Financial Sustainability
A high-margin, scalable B2G & B2B SaaS model providing 26x cost disruption over imported telemetry stations
MULTI-STREAM REVENUE MODEL
1. B2G Municipal Contracts (Primary):
• Annual monitoring & maintenance SLA with Disaster Management Centre (DMC) & Ministry of Irrigation.
• Retainer: LKR 1.5M – 2.5M / year per river basin catchment.
2. Insurance Data-as-a-Service (DaaS):
• Parametric flood risk verification API for insurers (Ceylinco, Sri Lanka Insurance) to validate flood damage claims.
• Fee: LKR 250,000 / month per institutional subscriber.
3. B2B Commercial Agriculture:
• Real-time microclimate soil-moisture feeds for tea/rubber estates in upstream Kegalle.
UNIT ECONOMICS & COST ADVANTAGE
Node Hardware Bill of Materials (BOM):
• ESP32 MCU + Sensor Interface: LKR 3,200
• Tipping Bucket Rain Gauge: LKR 4,800
• Solar Panel (5W) + TP4056 + Battery: LKR 3,500
• SIM800L / Enclosure / Mounting: LKR 3,000
• Total Per-Node CapEx: ~LKR 14,500 ($48 USD)
Market Disruption Benchmark:
• Imported Commercial Stations (OTT / Campbell Scientific): LKR 380,000 – 500,000 ($1,500 USD).
• Cost Advantage: 26x Cheaper! Allows dense spatial deployment across entire river reaches.
3-YEAR FINANCIAL PROJECTIONS
Pilot Phase (Year 1 - 50 Nodes):
• CapEx: LKR 725,000 | OpEx: LKR 450,000
• Projected Revenue: LKR 2.2M (B2G Pilot + Grant)
• Year 1 ROI: ~87.5% (Break-even in Month 8)
Growth Phase (Year 2 - 150 Nodes):
• Annual Revenue: LKR 5.8M | Net Margin: 48%
• Onboard 2 major agricultural/insurance clients.
Scale Phase (Year 3 - 450 Nodes National):
• Annual Revenue: LKR 14.5M | Net Margin: 56%
• Multilateral donor funding (World Bank / ADB Climate Resilience Facility).
SLIIT CDAP R26-IT-162 | FloodSense AI (Kelani River Basin Early Warning) | Slide 11 of 13

## Slide 12
DEPLOYMENT ROADMAP & SOCIAL IMPACT
Phased National Rollout Plan & Sustainable Community Resilience
From Kelani river basin pilot to a nationwide disaster early warning network protecting 11M+ citizens
PHASE 1: PILOT DEPLOYMENT (YEAR 0–1)
• Deploy 50 solar IoT nodes across high-risk Kelani reaches (Sedawatta, Hanwella, Kaduwela).
• Integrate with Disaster Management Centre (DMC) emergency operations room.
• Validate live ML model accuracy against actual 2026/2027 monsoon events.
• Target Beneficiaries: 500,000 vulnerable riverine citizens in Western Province.
PHASE 2: BASIN-WIDE EXPANSION (YEAR 2)
• Expand network to 150 nodes covering the entire Kelani Ganga catchment.
• Deploy localized village siren controllers in flood-prone Grama Niladhari divisions.
• Onboard parametric insurance partners for automated agricultural crop loss payouts.
• Train local youth technicians for routine hardware maintenance.
PHASE 3: NATIONAL SCALE (YEAR 3–5)
• Replicate architecture across other disaster-prone river basins (Kalu Ganga, Gin Ganga, Nilwala Ganga).
• Total Network: 450+ autonomous solar IoT nodes covering 11 Million people.
• Partner with UNDP, World Bank Climate Adaptation Fund, and Asian Development Bank (ADB).
• Social Mission: 100% free SMS warnings for registered low-income households.
SLIIT CDAP R26-IT-162 | FloodSense AI (Kelani River Basin Early Warning) | Slide 12 of 13

## Slide 13
CONCLUSION & TRANSITION TO DEMONSTRATION
Key Research Contributions & Live Demonstration Sequence
Transforming theoretical machine learning into an actionable, life-saving early warning system
RESEARCH CONTRIBUTIONS & VALUE DELIVERED
1. Micro-Catchment Spatial Disruption: Solved the 25km synoptic forecasting resolution blind-spot using sub-kilometer calibrated edge IoT sensing.
2. Multi-Horizon Predictive ML: Engineered a LightGBM multi-output framework projecting 24h, 48h, and 72h rainfall depths (R² = 0.841, MAE = 2.84mm).
3. Two-Stage Inundation Intelligence: Deployed Distance-Based Dynamic Flood Risk (DFRS) evaluating occurrence, risk score, arrival time, and water depth.
4. 26x Cost Innovation & Commercial Feasibility: Low-cost LKR 14,500 solar nodes provide a financially sustainable, scalable business model for DMC and insurers.
5. Humanitarian Impact: Trilingual community alerting directly reduces evacuation response times, protecting lives and livelihoods.
LIVE TECHNICAL DEMONSTRATION
We invite the examination committee to observe the 10-minute live demonstration:
1. Live IoT Telemetry: ESP32 node publishing real-time tipping pulses over HiveMQ Cloud Broker.
2. AI Weather Fusion: FastAPI backend ingesting live Open-Meteo atmospheric variables.
3. Multi-Horizon Dashboard: Streamlit AI interface displaying 24h, 48h, 72h predictive curves.
4. Severe Storm Simulation: Injecting 250mm monsoonal burst into the live inference pipeline.
5. End-to-End React UI Sync: Executing Two-Stage XGBoost model live in the browser.
Thank you. We are ready to begin the demonstration.
SLIIT CDAP R26-IT-162 | FloodSense AI (Kelani River Basin Early Warning) | Slide 13 of 13